## Slide 1: Dig_volt

## Slide 2: Dig_volt
If we want to using FPGA design the digital voltage measuring module, we can use the ADC (Analog to Digital Converter) to do.
In this chapter, we using embedfire ADC to design the module, this ADC can measure -5V to 5V and transfer to 8 bit width digital data (0 – 255).
And the this ADC sampling clock max frequency is 32MHz.
ADC
Voltage 5V
8’b1111_1111
ADC
Voltage -5V
8’b0000_0000
FPGA
FPGA

## Slide 3: Objective
In this chapter, we want to generate digi_volt module and display the voltage by seven segment display, the value shows to three decimal places.
And re-zero the voltage value in first 1024 sampling clocks.
Sampling clock set to 12.5 MHz.
X
X
?.
?
?
?
V

## Slide 4: System

## Slide 5: Sub-module
using previous

## Slide 6: Waveform Graph – adc_1
First 1024 sampling clock is re-zero part, after rezero, sum_em raised

## Slide 7: Waveform Graph – adc_2
After sum_en raised, display the voltage data measured

## Slide 8: Simulation-adc
In test bench, median set to 125, OK.

## Slide 9: Simulation-adc_ -5V
Ad_data is 0, the volt = 16’d4999, and sign is 1’b1, shows in seven segment is -4.999, ok.

## Slide 10: Simulation-adc_0V
Ad_data is 125, the volt = 0 and sign is 1’b0, shows 0.000, OK.

## Slide 11: Simulation-adc_5V
Ad_data is 255, the volt = 4999 and sign is 1’b0, shows 4.999, OK.